## Slide 1
Your System
Start with your “System” in a box
And place a dashed box around it to symbolize your System’s boundary
For the purposes of this example, we’ll assume your System is some kind of car-like vehicle

## Slide 2
Then start listing things your “System” has to interact with…
…and place them in their own boxes…
…outside of the System boundary to show you do not have any design control over them.
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Capitalizing the things’ names in the boxes is also common practice

## Slide 3
Don’t place other boxes in the system boundary,
even if they’re a part of your System!
This will help you stay focused on the interactions with other things without committing to what your System is/has structurally
Try trusting the tool and learn about its value, before trying to break the tool.
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Your System
Gas Tank
Tires
Directional Lights

## Slide 4
Draw (rectangular) lines connecting the outer boxes with your system
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
It’s helpful in the next step, if you space your boxes out around the System box

## Slide 5
Start to label the lines with text about how the box item interacts with the System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Place this text to the end of the connecting line closest to box item
Write the text as if you were writing a short statement that started with the name of the box item and ends with your System: Cargo is “stored in” Your System
affects handling of
Using lowercase for these statements is common
support weight of
provide fuel for
stored in
runs in front of
Your System

## Slide 6
And at the same time label the lines with text about how your System interacts with the box items…
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
affects handling of
support weight of
provide fuel for
stored in
runs in front of
Your System
For clarity to tell where the statement starts, it’s common to expand the system boundary to encapsulate the statements starting at your System.
avoids, collides with
drives through
This reads “Your System drives through Weather”

## Slide 7
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
affects handling of
provide fuel for
obtain fuel from
stored in
runs in front of
avoids, collides with
drives through
No need to say essentially the same thing on both ends. Just pick one and the need is covered.
Connecting lines don’t have to have text on both sides, but one end of the line needs to have some text

## Slide 8
Your System
Roads
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
For multiple statements, don’t make multiple lines. Just separate the statements with a
comma
obtain fuel from
stored in
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
drives through
In situations where your System would have to do different things if it did an action itself, vs. if the outer box item did the same action, it’s good to repeat that action on both sides
Parking Spaces
In this case Your System has to both alert Other Vehicles of its actions and it has to be able to allow recognition of Other Vehicle’s alerts of their actions (Think about turn signals as an example)

## Slide 9
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
obtain fuel from
fit in, maneuver in and out of
stored in
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
drives through
fit in and out of
By saying “fit in and out of” we actually
mean that the System has to both physically fit in a parking space AND be able to be maneuvered in and out of the space. As these are significantly different needs, its recommended to split it into 2 statements

## Slide 10
At the same time you can also write text on how the System interacts with the box items
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Affects visibility of
Only connect the outer boxes with lines if you think that interaction will directly will affect how your System will be designed
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
fit in the lanes of, be able to take turns of,
Have necessary friction against without damaging
provide fuel for
obtain fuel from
fit in, maneuver in and out of
stored in
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
carries without damaging, handles a variety of sizes of
drives through

## Slide 11
As you may have noticed, the way the outer boxes connect to your System informs needs that your System must meet…
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Affects visibility of
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
support weight of
fit in the lanes of, be able to take turns of,
Have necessary friction against without damaging
obtain fuel from
fit in, maneuver in and out of
stored in
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
carries without damaging, handles a variety of sizes of
drives through
There is a constraint here you’ll have to find out more about
You have to deal with unwanted interactions too
State the “obvious” interactions too; helps to ensure you and others won’t forget them

## Slide 12
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Affects visibility of
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
support weight of
fit in the lanes of, be able to take turns of,
Have necessary friction against without damaging
provide fuel for
obtain fuel from
fit in, maneuver in and out of
stored in
safely transports, protects in a crash, reacts to commands effectively,
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
carries without damaging, handles a variety of sizes of
drives through
We’ll have to formally define what terms like “safely”, “easily” and “effectively” means later. As well as a way to measure them.
Connections also help identify potential Performance Criteria...
How well your system does these functions will have to be able to be evaluated
steer, sleep in, fit in, can get in and out of, listen to radio in, see environment while within, alert other vehicles to their actions,

## Slide 13
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Affects visibility of
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
support weight of
fit in the lanes of, be able to take turns of,
Have necessary friction against without damaging
provide fuel for
obtain fuel from
fit in, maneuver in and out of
stored in
steer, sleep in, fit in, can get in and out of, listen to radio in, see environment while within, alert other vehicles to their actions,
safely transports, protects in a crash, reacts to commands effectively,
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
carries without damaging, handles a variety of sizes of
drives through
Optionally, when there are a large number of interfaces, this can be cleaned up by replacing the text with a symbol and a matching
symbol legend
A
B
A
B
safely transports, protects in a crash, reacts to commands effectively
steer, sleep in, fit in, can get in and out of, listen to radio in, see environment while within, alert other vehicles to their actions

## Slide 14
Your System
Roads
Parking Spaces
Weather
Wildlife
Passengers
Cargo
Other Vehicles
Gas Stations
Affects visibility of
affects handling of
collides with, cut offs, passes, alerts to its actions & intensions, honks at,
support weight of
fit in the lanes of, be able to take turns of,
Have necessary friction against without damaging
provide fuel for
obtain fuel from
fit in, maneuver in and out of
stored in
runs in front of
alerts to its actions & intensions, avoids, passes, easily seen by,
avoids, collides with
carries without damaging, handles a variety of sizes of
drives through
Having a large number / variety of interfaces is also sometimes an indication that the outer boxes should be refined / split into more specific
items
A
B
safely transports, protects in a crash, reacts to commands effectively
steer, sleep in, fit in, can get in and out of, listen to radio in, see environment while within, alert other vehicles to their actions
A
B

## Slide 15
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Disabled Passengers
What makes different kinds of passengers important enough to separate into have their own box, is that each kind of passenger will have to be handled differently by the system.
Taking a step back to think more about these interactions reveals there are a number of important kinds of passengers
Pets
Your System

## Slide 16
Your System
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Disabled Passengers
What makes different kinds of passengers important enough to separate into have their own box, is that each kind of passenger will have to be handled differently by the system.
Taking a step back to think more about these interactions reveals there are a number of important kinds of passengers
Pets
One example interaction is shown although there are many. In order to safely transport each of these passenger types, the System will have to do something special.
safely
transports
safely
transports
safely
transports

## Slide 17
Your System
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Car Seats
Cargo
Disabled Passengers
Thinking about baby safety helps make the realization that Car Seats are a special type of Cargo that will need to be handled.
Pets
Cargo is kept as well to represent all other kinds of generic cargo
This triggers further brainstorming…

## Slide 18
Your System
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Car Seats
Cargo
Disabled Passengers
Pets
Baby’s make messes and so do pets, so we better think about all of the kinds of mess sources
Oil
Milk
Juice
French Fries
Mud
Vomit
The list could go on and on…

## Slide 19
Your System
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Car Seats
Cargo
Disabled Passengers
Pets
So instead of writing them all, we pick a subset such that if the System can handle that subset, it should be able to handle all the rest.
Oil
Milk
Juice
French Fries
Mud
Vomit
Representing all greasy and flammable substances
Representing all organic, smelly, and biohazard substances

## Slide 20
Your System
Local Roads
Speed Bumps
Parking Spaces
Multi-Lane Highways
Parking Garages
Toll Booths
Sharknado
Wildlife
Drivers
Adult Passengers
Children Passengers
Baby Passengers
Car Seats
Cargo
Pets
Roof Rack Items
Other Vehicles
Dept. of Motor Vehicles
Exit/Entry Ramps
Intersections
Pedestrians
Oil
Vomit
Disabled Passengers
Continuing this process reveals a lot of needed special interactions. A car-like system is certainly a complex one, and you may find more in this example than in your own System.
If your Context Diagram becomes too crowded, you may be able to split it into several. For example, here we suggest splitting the boxes into those objects that primarily interface with the interior and the exterior of the System. Other ways may be possible and could work just as well.
Snow
Fog

## Slide 21
Being thorough in your Context Diagram can be time consuming and even feel tedious if you’re not used to using this tool. But there are common ways to break up the work
After you have done some initial work (as shown in slide 12) and you want to explore parts of the diagram further, this becomes a great time to start to split up the work with your teammates. Each person can then create there own context diagram(s) for the parts they explored.
You can try to combine them all together later if you want, but at least recognize which outer boxes show up in multiple teammate’s work and compare the interactions discussed in all teammate’s work to help everyone have a clear idea of the interaction needs.