## Slide 1
CESYS526: Defining Interfaces
Cornell University College of Engineering
Instructions:
Use this template to create your own sequence diagram in order to show the interaction between your system’s subsystems during its operation.
To help you navigate through this PowerPoint:
  Slide 2 – Sequence Diagram Basic. This includes the minimum items you should include in your sequence diagram. Copy and paste from this slide to add components to your own sequence diagram. Do not attempt to make your sequence diagram fit exactly in this template as-is.
  Slide 3 – Sequence Diagram Advanced. You may find it helpful to use this as a starting point for adding more detail to your diagram. You can copy and paste from the slide to add these additional components to your own sequence diagram. Do not attempt to make your sequence diagram fit exactly in this template as-is. This slide also shows:
    Common optional elements of operational flow & logic
    An option to include an operational description along the side of the sequence diagram to indicate what activities are being performed within the activation boxes.
  Slide 4 – Sequence Diagram Example. This shows an example of sequence diagram that follows from the course’s autonomous robotic example. To make the example simple to follow, only the involvement of the Sensor Filtering & Path Planning subsystems and an exterior system Mission Control are shown.
  Slide 5 – Sequence Diagram Example with Callouts: This includes common names of sequence diagram elements for your reference.
  Slide 6 – Sequence Diagram Example Relating Elements with Flow Notes: This includes arrows that connect each operational description on the right with the diagram element on the left that is being explained by the description.
To submit this assignment, please refer to the instructions in the course.
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.

## Slide 2
Sequence Diagram Template – Basic
[y >100]
5. Arrow, label, box to next box
Subsystem 2
Subsystem 1
initial msg.
  sensor data (freq., accuracy)
return
message Q
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.

## Slide 3
alt
opt
[else]
[x > 100]
loop
initial msg
specific output
return value
[shutdown]
close
activate
command
[y > 100]
interface(add’l Info)
Subsystem 1
Subsystem 2
Exterior System
Sequence Diagram Template – Advanced
Activity Description
An optional informal description of what is occurring within system the activation boxes may be shown on the side
  Indentation may be used to visually highlight which activities are occurring within frames
data D
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.

## Slide 4
Path Planning Update Sequence for Sensor Filtering and Path Planning Subsystems
sensor data and destination update received
loop until the destination is reached
convert the data into a new map
send the map with an updated time stamp
attempt to find a path to the destination
  if a valid path is found
  send the planned route to Mission Control
  Mission Control verifies the route
  Sends route verification result
  Send record of additional mission control information
  else
  calculate local recon path to aid in finding new alternate route
end if
end loop
Destination is reached so enter standby mode
shut down path planning operations to conserve energy
alt
opt
[else]
[valid path found]
loop
new data & destination
planned route
Go/No Go approval
[standby mode]
close
activate
command
[destination reached]
map (update time)
Sensor Filtering
Path Planning
Mission Control
Sequence Diagram Sample – Advanced
approval record
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.

## Slide 5
Path Planning Update Sequence for Sensor Filtering and Path Planning Subsystems
sensor data and destination update received
loop until the destination is reached
convert the data into a new map
send the map with an updated time stamp
attempt to find a path to the destination
  if a valid path is found
  send the planned route to Mission Control
  Mission Control verifies the route
  Sends route verification result
  Send record of additional mission control information
  else
  calculate local recon path to aid in finding new alternate route
end if
end loop
Destination is reached so enter standby mode
shut down path planning operations to conserve energy
alt
opt
[else]
[valid path found]
loop
new data & destination
planned route
Go/No Go approval
[standby mode]
close
activate
command
[destination reached]
map (update time)
Sensor Filtering
Path Planning
Mission Control
Sequence Diagram Sample – with Callouts
approval record
participant
self call
return
activation
lifeline
frame
guard
message
found message
operator
deletion
operator
data
tadpole
parameter
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.

## Slide 6
alt
opt
[else]
[valid path found]
loop
new data & destination
planned route
Go/No Go approval
[standby mode]
close
activate
command
[destination reached]
map (update time)
Sensor Filtering
Path Planning
Mission Control
Path Planning Update Sequence for Sensor Filtering and Path Planning Subsystems
sensor data and destination update received
loop until the destination is reached
convert the data into a new map
send the map with an updated time stamp
attempt to find a path to the destination
  if a valid path is found
  send the planned route to Mission Control
  Mission Control verifies the route
  Sends route verification result
  Send record of additional mission control information
  else
  calculate local recon path to aid in finding new alternate route
end if
end loop
Destination is reached so enter standby mode
shut down path planning operations to conserve energy
approval record
© 2019 eCornell. All rights reserved. All other copyrights, trademarks, trade names, and logos are the sole property of their respective owners.
Sequence Diagram Sample – Relating Elements with Flow Notes